## Slide 1: Finding the Path
Descriptions of the “Path” class of functions

## Slide 2: Many applications require a reference path
For example, roads are a form of path. The task of driving is to stay on the road, which means that a vehicle’s position relative to the path must be measured.

## Slide 3: Definitions of terms
Station
Stations
Path
Paths
Traversal
Traversals

## Slide 4: What is a path?
An XY path is just XY points saved as an array that denote the locations we are trying to follow. We can save it as a single array, or even an array of arrays such as:
paths{1} = [
8.1797 8.6006
8.4101 15.8892
10.0230 25.5102
10.4839 39.7959];

## Slide 5: Sometimes we want more information, so we define something called a “traversal”
It includes subfields that are routinely used, particularly the Station and Yaw. We convert from Path to Traversals often, so a function exists that will fill in a Traversal given a Path.
function traversal = fcn_Path_convertXYtoTraversalStructure(X,Y)
% fcn_Path_convertXYtoTraversalStructure
% Takes XY positions and creates a traversal structure
%
% FORMAT:
%
% traversal = fcn_Path_convertXYtoTraversalStructure(X,Y)
%
% INPUTS:
%
% X: an N x 1 vector of X positions
% Y: an N x 1 vector of X positions
%
% OUTPUTS:
%
% traversal: a sttructure containing the following fields
% - X: a duplicate of the input X
% - Y: a duplicate of the input Y
% - Z: a zero array the same length as the input X
% - Diff: a [N x 2] array that is the change in X and Y
% (front-padded with [0 0])
% - Station: the XY distance traveled up to the current point
% (starting with 0 at the first point)
% - Yaw: the calculated yaw angle (radians) from the Diff
% calculated by arctangent of the Diff result
% (thus - it is front-padded with NaN)

## Slide 6: We’re often creating paths, but for dummy “starter” paths we have a function
Note: a click-to-draw function also exists that allows interactive creation of paths.
% Fill in some dummy data
paths = fcn_Path_fillSamplePaths;

## Slide 7: We often collect traversals into data structures as shown below, and often need to plot them. A function exists for this.
% script_test_fcn_Path_plotPathXY.m
% Fill in some dummy data
paths = fcn_Path_fillSamplePaths;
% Show how the function works
for i_traveral = 1:length(paths)
traversal = fcn_Path_convertXYtoTraversalStructure(paths{i_traveral}(:,1),paths{i_traveral}(:,2));
data.traversal{i_traveral} = traversal;
end
% Call the plot command to show results in XY
fig_num = 12;
fcn_Path_plotPathXY(data,fig_num);

## Slide 8: Similarly, we often want to plot the yaw and a function exists for this too
% script_test_fcn_Path_plotPathYaw.m
% Fill in some dummy data
paths = fcn_Path_fillSamplePaths;
% Convert paths into traversals
for i_traveral = 1:length(paths)
traversal = fcn_Path_convertXYtoTraversalStructure(paths{i_traveral}(:,1),paths{i_traveral}(:,2));
data.traversal{i_traveral} = traversal;
end
% Call the plot command to show how it works.
figure(11);
fcn_Path_plotPathYaw(data);

## Slide 9: Basic Path Operations Include
Finding the intersection of segments:
Snapping a point onto a path:
Projecting from a path normally outward
Generating random traversals about a reference traversal
Trimming out sections of traversals given certain station points
These basic functions are described below.

## Slide 10: Finding the intersection of segments

## Slide 11: The most basic path operation is finding the intersection of a path segment rooted at p and extending to p+r, with a sensor rooted at q and extending to p+s.
Details can be found at: https://stackoverflow.com/questions/563198/how-do-you-detect-where-two-line-segments-intersect

## Slide 12: This capability is implemented in fcn_Path_findProjectionHitOntoPath.m
% fcn_Path_findProjectionHitOntoPath calculates hits between a sensor
% projection and a path, returning the distance and location of the hit.
%
% FORMAT:
%
% [distance,location] = ...
% fcn_Path_findProjectionHitOntoPath(path,...
% sensor_vector_start,sensor_vector_end,...
% (flag_search_type),(fig_num))
%
% INPUTS:
%
% path: an N x 2 vector containing the X,Y points of the path to be
% checked for intersections
%
% sensor_vector_start: a 1 x 2 vector containing the X,Y points of the
% sensor's start location
%
% sensor_vector_end: a 1 x 2 vector containing the X,Y points of the
% sensor's end location
%
% (OPTIONAL INPUTS)
% flag_search_type: an integer specifying the type of search.
%
% 0: return distance and location only if the given
% sensor_vector overlaps the path (this is the default)
%
% 1: return distane and location if any projection of the sensor
% vector, in any direction, hits the path (in other words, if
% there is any intersection). Note that distance returned will
% be negative if the nearest intersection is in the opposite
% direction of the given sensor vector.
%
% fig_num: a figure number to plot results. Turns debugging on.
%
% OUTPUTS:
%
% distance: a 1 x 1 scalar representing the distance to the closest
% intersection of the sensor with the path
%
% location: a 1 x 2 vector of the X,Y location of intersection point

## Slide 13: This method requires the definition of the cross product
Define the 2-dimensional vector cross product v × w to be vx wy − vy wx.
%% Calculate cross products
function result = crossProduct(v,w)
result = v(:,1).*w(:,2)-v(:,2).*w(:,1);
end

## Slide 14: The method used is to consider fractions of the path and of the sensor vectors
Suppose the path segment runs from p to p + r and sensor starts from q and extends to q + s. Then any point on the first line is representable as p + t r (for a scalar parameter t) and any point on the second line as q + u s (for a scalar parameter u).

## Slide 15: The two lines intersect if we can find t and u such that:
p + t r = q + u s
To solve, cross both sides with s, getting
(p + t r) × s = (q + u s) × s
And since s × s = 0, this means
t (r × s) = (q − p) × s
And therefore, solving for t:
t = (q − p) × s / (r × s)

## Slide 16: We can solve for u similarly:
(p + t r) × r = (q + u s) × r
u (s × r) = (p − q) × r
u = (p − q) × r / (s × r)
To reduce the number of computation steps, it's convenient to rewrite this as follows (remembering that s × r = − r × s):
u = (q − p) × r / (r × s)

## Slide 17: If the lines are parallel then r × s = 0
If (q − p) × r = 0, then the lines are co-linear as well. NOTE: this is NOT checked for in the code!
In this case, express the endpoints of the second segment (q and q + s) in terms of the equation of the first line segment (p + t r):
t0 = (q − p) · r / (r · r)
t1 = (q + s − p) · r / (r · r) = t0 + s · r / (r · r)
If the interval between t0 and t1 intersects the interval [0, 1] then the line segments are collinear and overlapping; otherwise they are collinear and disjoint.
Note that if s and r point in opposite directions, then s · r < 0 and so the interval to be checked is [t1, t0] rather than [t0, t1].

## Slide 18: If parallel and non-intersecting?
If r × s = 0 and (q − p) × r ≠ 0, then the two lines are parallel and non-intersecting

## Slide 19: What if they intersect?
If r × s ≠ 0 and 0 ≤ t ≤ 1 and 0 ≤ u ≤ 1, the two line segments meet at the point p + t r = q + u s. Otherwise, the two line segments are not parallel but do not intersect.
Credit: this method is the 2-dimensional specialization of the 3D line intersection algorithm from the article "Intersection of two lines in three-space" by Ronald Goldman, published in Graphics Gems, page 304. In three dimensions, the usual case is that the lines are skew (neither parallel nor intersecting) in which case the method gives the points of closest approach of the two lines.

## Slide 20: Intersections at the end-points of the path
If intersections occur at the end-points of a path segment, then results can be ambiguous because t = 0 or t=1. In these cases, can have weird situations if we omit this, e.g. the following:
((0<t).*(1>t).*(0<u).*(1>u));
The result of this condition is that NO intersection would be detected

## Slide 21: If we correct the t-range, then the intersection is found
good_vector = ((0<=t).*(1>=t).*(0<u).*(1>u));

## Slide 22: Similarly, this form with the u range not including 0 or 1 can miss paths that barely hit the sensor at start or end
Missing the origin is a particularly bad error as it would cause one to miss overlapping paths

## Slide 23: Here’s the correct result
good_vector = ((0<=t).*(1>=t).*(0<=u).*(1>=u));

## Slide 24: Example 1: A simple example
%% Simple test 1 - a simple intersection
fprintf(1,'Simple intersection result: \n');
path = [0 10; 10 10];
sensor_vector = [2 1; 5 15];
fig_debugging = 2343;
[distance,location] = ...
fcn_Path_findProjectionHitOntoPath(path,sensor_vector,fig_debugging);
print_results(distance,location);
See: script_test_fcn_Path_findProjectionHitOntoPath.m

## Slide 25: Example 2: Not intersecting
%% Simple test 2 - no intersections
fprintf(1,'No intersection result: \n');
path = [-4 10; 2 10];
sensor_vector = [0 0; 5 12];
fig_debugging = 2343;
[distance,location] = ...
fcn_Path_findProjectionHitOntoPath(path,sensor_vector,fig_debugging);
print_results(distance,location);
See: script_test_fcn_Path_findProjectionHitOntoPath.m

## Slide 26: Example 3: Multiple line segments
%% Simple test 3 - multiple intersections
fprintf(1,'Multiple intersections result: \n');
path = [0 10; 10 10; 0 6; 10 6; 0 2];
sensor_vector = [0 0; 5 12];
fig_debugging = 2343;
[distance,location] = fcn_Path_findProjectionHitOntoPath(...
path,sensor_vector,fig_debugging);
print_results(distance,location);
See: script_test_fcn_Path_findProjectionHitOntoPath.m

## Slide 27: In some applications, the “length” of the sensor vector is irrelevant. One simply wants to know any location, in any direction, where an intersection could occur.
The flag_search_type variable can be set to 1 (instead of 0, default) to specify that any intersection will work. Here’s an example with a sensor vector of length 2. If an “unlimited” search is used, a hit is detected with either positive or negative distance.
flag_search_type = 0
flag_search_type = 1

## Slide 28: Snapping a point onto a path

## Slide 29: One of the basic path operations is snapping from a query point onto a path
The goal is to find the point ON A PATH that is “closest” to the query point. One way to do this is to find the closest vertex on a path to a query point. That closest vertex is connected to 1 or 2 other points.
If 2 points, we then check which of these 2 points is closest to the query point,
and use that to define a segment. We then project from that segment to the query point.

## Slide 30: This functionality is implemented in the MATLAB function: fcn_Path_snapPointOntoPath
%% BASIC example 1.2 - works
point = [1.4 1.3]; % Define the query point
pathXY = [0 0; 0.5 0.2; 0.9 0.9; 1.5 0.6; 3 0]; % Define an XY path
pathSXY = fcn_Path_convertXYtoSXY(pathXY(:,1),pathXY(:,2)); % Convert to SXY path
fignum = 112; % Define the figure number
% Snap the point onto the path
[closest_path_point,s_coordinate,...
first_path_point_index,second_path_point_index,...
percent_along_length] = ...
fcn_Path_snapPointOntoPath(point, pathSXY,fignum);
% Print results to the workspace
fprintf(1,'Figure: %d\n',fignum);
fprintf(1,'\t\t Closest point is: %.2f %.2f \n',...
closest_path_point(1,1),closest_path_point(1,2));
fprintf(1,'\t\t Matched to the path segment given by indices %d and %d, \n',...
first_path_point_index,second_path_point_index);
fprintf(1,'\t\t S-coordinate is: %.2f, \n',...
s_coordinate);
fprintf(1,'\t\t percent_along_length is: %.2f\n',percent_along_length);
(Worspace shows)
Figure: 112
Closest point is: 1.14 0.78
Matched to the path segment given by indices 3 and 4,
S-coordinate is: 1.61,
percent_along_length is: 0.40

## Slide 31: This breaks if the nearest segment is not the one with two closest endpoints
Figure: 113
Closest point is: 1.09 1.23
Matched to the path segment given by indices 2 and 3,
S-coordinate is: 1.73,
percent_along_length is: 1.48
%% BASIC example 1.3 - breaks
point = [1.5 1];
pathXY = [0 0; 0.5 0.2; 0.9 0.9; 3 0];
pathSXY = fcn_Path_convertXYtoSXY(pathXY(:,1),pathXY(:,2));
fignum = 113;
% Snap the point onto the path
[closest_path_point,s_coordinate,...
first_path_point_index,second_path_point_index,...
percent_along_length] = ...
fcn_Path_snapPointOntoPath(point, pathSXY,fignum);
% Print results to the workspace
fprintf(1,'Figure: %d\n',fignum);
fprintf(1,'\t\t Closest point is: %.2f %.2f \n',...
closest_path_point(1,1),closest_path_point(1,2));
fprintf(1,'\t\t Matched to the path segment given by indices %d and %d, \n',...
first_path_point_index,second_path_point_index);
fprintf(1,'\t\t S-coordinate is: %.2f, \n',...
s_coordinate);
fprintf(1,'\t\t percent_along_length is: %.2f\n',percent_along_length);

## Slide 32: One idea to fix these errors might be to check whether the “snap” point is on a segment, but there are queries that occur where the result would be on neither segment. For example:

## Slide 33: In vehicle preview-based control, the ambiguity of the snap point can cause different errors depending on whether the projection is from the path to vehicle, or vehicle to path
Vehicle
Vehicle
Vehicle
Look ahead
Snap point
Snap is orthogonal to preview, e.g. projection is from vehicle to path
Snap is orthogonal to path, e.g. projection is from path to vehicle

## Slide 34: When snapping points onto paths, if we include too much of a path, particularly one turned back toward itself, we can get incorrect snap points.

## Slide 35: Projecting from a path normally outward

## Slide 36: A common operation is to seek vectors that are normal to a path at given station points
This is used in calculating nearby paths, in projecting paths sideways, and similar operations

## Slide 37: This capability is implemented in fcn_Path_findProjectionHitOntoPath.m
function [unit_normal_vector_start, unit_normal_vector_end] = ...
fcn_Path_FindOrthogonalPathVectorsAtStations(stations,central_traversal, varargin)
% fcn_Path_FindOrthogonalPathVectorsAtStations
% Given a central traversal and a set of stations along that traversal,
% finds the unit normal vector on the central traveral at each station
% point.
%
% FORMAT:
%
% [unit_normal_vector_start, unit_normal_vector_end] = ...
% fcn_Path_FindOrthogonalPathVectorsAtStations(...
% stations,central_traversal,...
% (flag_rounding_type),(fig_num));
%
% INPUTS:
%
% stations: an N x 1 vector containing the station on the central
% traversal where the projections should take place
%
% central_traversal: a traversal structure that specifies the path
% where projections to other paths are taking place.
%
% (OPTIONAL INPUTS)
% flag_rounding_type: a flag to indicate which type of projection is
% used, especially when stations are located at the end-points of
% segments within the nearby_traversal. When stations are at the
% end-points of segments, the normal vector is undefined as it depends
% on whether to use the prior or subsequent segment, or some
% combination of these.
%
% Note that the very first point always uses projections from the
% following segement, and the very last point always uses the prior.
% Otherwise, the flag determines behaviors for endpoints of internal
% segments. The options include:
%
% flag_rounding_type = 1; % This is the default, and indicates
% that the orthogonal projection of an endpoint is created by the
% PRIOR segment leading up to each station query point.
%
% flag_rounding_type = 2; % This indicates that the orthogonal
% projection of an endpoint is created by the FOLLOWING segment
% after each station query point.
%
% flag_rounding_type = 3; % This indicates that the orthogonal
% projection, ONLY if the station query falls at the joining point
% between two segments (e.g. is on the "joint"), then the
% projection is created by averaging the vector projections
% created from the PRIOR segment and FOLLOWING segment.
%
% flag_rounding_type = 4; % This indicates that the orthogonal
% projections along segments should be calculated at the midpoints
% of each segment, and then for each station qeuary, the vector
% projections are interpolated from their prior and subsequent
% vectors.
%
% fig_num: a figure number to plot results. Turns debugging on.
%
% OUTPUTS:
%
% unit_normal_vector start: a Nx2 vector containing [X1 Y1]
% coordinates as columns, where the [X1 Y1] represents the location of
% the start point of the vector, on the path.
%
% unit_normal_vector_end: a Nx2 vector containing the [X2 Y2] location
% of the end point of the unit vector. On both outputs, there are N
% rows, one row for each station.
%

## Slide 38: Here are some examples:
See: script_test_fcn_Path_FindOrthogonalPathVectorsAtStations.m

## Slide 39: Particularly at an internal vertex, it can be very unclear what to use as a normal vector. Here are 4 options that 1) use previous, 2) use following, 3) average both only at vertex, and 4) average everywhere

## Slide 40: Generating random traversals

## Slide 41: Using normal projections, a common task is to generate random traversals about a given traversal
See: fcn_Path_fillRandomTraversalsAboutTraversal.m and script_test_fcn_Path_fillRandomTraversalsAboutTraversal.m

## Slide 42: One can choose different smoothness factors or the number of trajectories produced

## Slide 43: One can change the standard deviations

## Slide 44: One can also change the number of points to use to generate each random traversal

## Slide 45: Plotting variance bands about a traveral

## Slide 46: The orthogonal projections can also be used to plot the standard deviation about a traversal
See: script_test_fcn_Path_plotPathXYWithVarianceBands.m

## Slide 47: Note that this function, fcn_Path_plotPathXYWithVarianceBands inherets the band color from plotting, so that multiple traversals can be put on the same figure.

## Slide 48: Calculating the variance of a traversal

## Slide 49: The variance of a single traversal is a measure of how much it bends at each segment, as a distance offset.
This is useful to estimate the error in decimation of a path, as this variance becomes smaller with finer decimations.
See: script_test_fcn_Path_calcSingleTraversalStandardDeviation

## Slide 50: Trimming a path

## Slide 51: To force a query to include only a short part of a path, we use: fcn_Path_findPathSXYSegment.m
See script_test_fcn_Path_findPathSXYSegment for this demo

## Slide 52: Path Averaging Methods

## Slide 53: One of the more useful ways to create permanent paths is to average ones followed earlier. These naturally occurring paths are called “desire lines”.

## Slide 54: The averaging process seems obvious, but it depends on metrics of distance
There are many!
Averaging points with the same station for different paths
Averaging the closest points from other paths to given points
Averaging points found by orthogonal projection from a path

## Slide 55: An issue with averaging different paths by merging them at the same stations is that the stations can be very different due to paths weaving.
See: script_test_fcn_Path_convertXYtoSXY.m

## Slide 56: This discrepancy in station distances is why lanes on track and field have staggered starts. The inside line would be shorter than the outside lane if everyone started at the same line.

## Slide 57: The “closest point” method finds the closest point on a nearby path to the central path. It then finds the associated line segment on the nearby path, and then projects FROM the line segment back to the central path.
Note: the figures in this section can be produced by running: script_test_fcn_Path_findClosestPointsFromPath.m

## Slide 58: This method has the advantage of generating expected results even when the queries “graze” nearby paths

## Slide 59: But this method gives unexpected results when the segment’s closest location is not actually on the segment.

## Slide 60: Generally, the “closest point” method gives expected results when applied to adjacent paths

## Slide 61: The problem with closest point is that the directions of the contributions can be unclear, e.g. the nearby path may be ahead or behind the station points on the central path.

## Slide 62: Orthogonal projection takes a “central” trajectory, and then projects orthogonally from that trajectory at given stations to find where it hits nearby trajectories.
%% BASIC example 1 - parallel lines, query is in middle area
stations = 1; % Define the station
% Create a dummy central path and convert it to a traversal
central_path = [0 0; 2 0];
central_traversal = fcn_Path_convertXYtoTraversalStructure(central_path(:,1),central_path(:,2));
% Define a "nearby" path and convert it to a traversal
nearby_path = [0 4; 2 4];
nearby_traversal = fcn_Path_convertXYtoTraversalStructure(nearby_path(:,1),nearby_path(:,2));
% Calculate the closest point and distance on the nearby path
[closest_path_point,distances] = ...
fcn_Path_FindOrthogonalHitFromPathToPath(stations,central_traversal,nearby_traversal);
print_results(stations,closest_path_point,distances);

## Slide 63: The approach gives the intersection point for arbitrary segments nearby the central trajectory
%% BASIC example 2 - angled line segment adjacent to endpoint query
stations = 1;
central_path = [0 0; 2 0];
central_traversal = fcn_Path_convertXYtoTraversalStructure(central_path(:,1),central_path(:,2));
nearby_path = [0 4; 2 7];
nearby_traversal = fcn_Path_convertXYtoTraversalStructure(nearby_path(:,1),nearby_path(:,2));
[closest_path_point,distances] = ...
fcn_Path_FindOrthogonalHitFromPathToPath(stations,central_traversal,nearby_traversal);
print_results(stations,closest_path_point,distances);

## Slide 64: We define a “miss” to even include “grazing” from one trajectory to another
%% BASIC example 3 - angled line segment adjacent to endpoint query but near-miss
stations = 10;
central_path = [0 0; 10 0];
central_traversal = ...
fcn_Path_convertXYtoTraversalStructure(central_path(:,1),central_path(:,2));
nearby_path = [0 4; 10 7];
nearby_traversal = ...
fcn_Path_convertXYtoTraversalStructure(nearby_path(:,1),nearby_path(:,2));
[closest_path_point,distances] = ...
fcn_Path_FindOrthogonalHitFromPathToPath(stations,central_traversal,nearby_traversal);

## Slide 65: A challenge with query stations is that the orthogonal projection is unclear. At the start and end, we use the segment ahead and behind these points.
NOTE: the code for the images here and in the next few slides can be found in: script_test_fcn_Path_FindOrthogonalHitFromPathToPath.m

## Slide 66: As noted before in the orthogonal projection, the normal vectors are unclear at vertex points, and the path intersections can change depending on which type of averaging is used.

## Slide 67: The same challenge arises for queries to the involuted area

## Slide 68: One result of this process is that some areas of a nearby path may receive very poor sampling. Generally, portions of nearby paths that are parallel are sampled well, but perpendicular are not.

## Slide 69: For orthogonal projection, the option of averaging at the vertex appears to give the best results

## Slide 70: The key advantage of the orthogonal projection is that every query “cuts” adjacent paths as one would expect.

## Slide 71: The function, fcn_Path_FindOrthogonalScatterFromPathToPaths implements this cutting process at given stations
See: script_test_fcn_Path_FindOrthogonalScatterFromPathToPaths for examples

## Slide 72: This allows one to average adjacent paths along each cut to produce an average path.
This is implemented in fcn_Path_findAveragePathViaOrthogonalProjection.m

## Slide 73: The process of averaging has to avoid averaging paths that are nearby but not adjacent in the s-coordinate. Otherwise, the average will bias toward the alternate paths and may even “wander” at the intersections.
script_test_fcn_Path_findAveragePath.m

## Slide 74: To force a query to include only a short part of a path, we use: fcn_Path_findPathSXYSegment.m as mentioned earlier.
See script_test_fcn_Path_findPathSXYSegment for this demo

## Slide 75: A comparison of the averaging methods shown here reveals that orthogonal projection cross-sections appear to work the best
See: script_test_fcn_Path_findAveragePath.m

## Slide 76: Note that the orthogonal averaging function has the additional outputs of distance and XY hit points of the nearby paths, which allow statistics, detailed point analysis, and advanced plotting.
See: script_test_fcn_Path_findAveragePath